## Slide 1
SSH Programming with Python and Paramiko

## Slide 2
#Basic Python install in Linux
apt-get update
apt-get install python -y
apt-get install build-essential libssl-dev libffi-dev -y
apt-get install python-pip -y
apt-get install python-dev -y
pip install cryptography
pip install paramiko

## Slide 3
BASIC SSH TEMPLATE
import paramiko
import time
ip_address = "192.168.122.72"
username = "ant"
password = "cisco"
ssh_client = paramiko.SSHClient()
ssh_client.set_missing_host_key_policy(paramiko.AutoAddPolicy())
ssh_client.connect(hostname=ip_address,username=username,password=password)
print "Successful connection", ip_address
# Insert IOS commands in this section
ssh_client.close

## Slide 4
remote_connection = ssh_client.invoke_shell()
remote_connection.send("configure terminal\n")
remote_connection.send("int loop 0\n")
remote_connection.send("ip address 1.1.1.1 255.255.255.255\n")
remote_connection.send("int loop 1\n")
remote_connection.send("ip address 2.2.2.2 255.255.255.255\n")
remote_connection.send("router ospf 1\n")
remote_connection.send("network 0.0.0.0 255.255.255.255 area 0\n")
for n in range (2,21):
print "Creating VLAN " + str(n)
remote_connection.send("vlan " + str(n) + "\n")
remote_connection.send("name Python_VLAN " + str(n) + "\n")
time.sleep(0.5)
remote_connection.send("end\n")
time.sleep(1)
output = remote_connection.recv(65535)
print output
IOS Commands
Add IP addresses
- Add VLANs